## Slide 1
The U.S. Army Pathfinder School
Nomenclature

## Slide 2: Common Sling Load Equipment Note: Students are required to know both proper nomenclature and all rated capacities. Information (in parenthesis) is not testable.

## Slide 3: Aerial Delivery Sling Type XXVI Multi-Loop Line
Rated capacity |  | 
# of loops | Pendant | Lifting Provision
2 | 8,900 lbs | 5,600 lbs
3 | 13,500 lbs | 8,500 lbs
4 | 17,800 lbs | 11,200 lbs
6 | 27,000 lbs | 17,000 lbs

## Slide 4: Aerial Delivery Sling Type XXVI Multi-Loop Line
Lengths | 
# of loops | Lengths Available
2 | 3’, 9’, 11’, 12’, 16’, 20’, and 120’
3 | 60’ and 140’
4 | 3’, 9’, 11’, 12’, 16’, 20’, and 28’
6 | 60’ and 120’

## Slide 5
1
2
3
4
5
3 Foot Apex Ring or Donut Ring-Rated capacity: 10,000 lbs
Type IV Connector Link-Rated capacity: 12,500 lbs
Base Plate
Aluminum Buffers
Locking Plate
Cotton Buffer
3 Foot Apex Ring or Donut Ring (Aerial Delivery Sling with Type IV Connector Link)
6

## Slide 6
1
1. Two Point Link Assembly- Rated capacity: 25,000 lbs
Two Point Link Assembly

## Slide 7
Suspension Clevises
1
2
3
Small Suspension Clevis- Rated capacity: 6,250 lbs, Lifting provision: 3,750 lbs
Medium Suspension Clevis- Rated capacity: 6,250 lbs, Lifting provision: 3,750 lbs
Large Suspension Clevis- Rated capacity: 12,500 lbs, Lifting provision: 7,875 lbs
Nut
Bolt
4
5
4
5
4
5

## Slide 8
Cargo Tie-Down Equipment
2
1
3
A7A Strap- Rated capacity: 500 lbs
Friction Adapter
CGU-1/B- Rated capacity: 5,000 lbs

## Slide 9
1
2
3
4
15 Foot Tie-Down Strap (Dacron Lashings)- Rated capacity: 10,000 lbs
D-Ring
Silver Load Binder- Rated capacity: 5,000 lbs
Black Load Binder- Rated capacity: 10,000 lbs
Cargo Tie-Down Equipment

## Slide 10
1
2
3
Screw Pin
Cotter Pin
5/8in Screw Pin Clevis- Rated Capacity: 4,420 lbs
Cargo Tie-Down Equipment

## Slide 11
10,000LBS Sling Leg
1
2
3
4
10,000 lbs Apex Fitting- Rated capacity: 10,000 lbs
10,000 lbs Sling Leg- Rated capacity: 2,500 lbs
Chain
Grabhook Assembly

## Slide 12
25,000 LBS Sling Leg
1
2
3
4
25,000 lbs Apex Fitting- Rated capacity: 25,000 lbs
25,000 lbs Sling Leg- Rated capacity: 6,250 lbs
Chain
Grabhook Assembly

## Slide 13
Apex Fitting
1a
1b
2
2
3a
3b
4
4
5
5
6
6
Apex Fitting Pin- Rated capacity: 10,000 lbs=1 1/8 Inch (1a), 25,000 lbs=1 ½ Inch (1b)
Apex Spacer
Apex Shackle- Rated capacity: 10,000 lbs (3a) AND 25,000 lbs (3b)
Castellated Nut
3/8 Inch Drilled Bolt
Cotter Pin

## Slide 14
Grabhook Assembly
1
2
3
4
5
7
8
9
Bolt and dome nut/locking nut 6. Eye
Keeper 7. Coupling Link
Hook 8. Spacer
Pin 9. Snap Ring
Yoke
6
4
7

## Slide 15
25,000 LBS Cargo Hook Reach Pendant
1
2
3
4
Large Looped End (Towards the load)
Directional Arrow
Handle
Small Looped End (Towards the aircraft)

## Slide 16
11,000LBS Cargo Hook Reach Pendant
1
2
3
4
Large Looped End (Towards the load)
Directional Arrow
Handle
Small Looped End (Towards the aircraft)

## Slide 17
Polyester Round Sling
1
1. Identification Tag (At least one must be present and legible)
1

## Slide 18
Polyester Round Sling
Rated capacity by hitch type |  |  |  |  | 
Length | Color | Choked | Vertical | Basket | Sling Weight
8’ | Green | 4,200 lbs | 5,300 lbs | 10,600 lbs | 4 lbs
17’ | Green | 4,200 lbs | 5,300 lbs | 10,600 lbs | 10 lbs
8’ | Yellow | 6,700 lbs | 8,400 lbs | 16,800 lbs | 5 lbs
17’ | Yellow | 6,700 lbs | 8,400 lbs | 16,800 lbs | 11 lbs
30’ | Red | 10,600 lbs | 13,200 lbs | 26,400 lbs | 26 lbs
65’ | Blue | 17,000 lbs | 21,200 lbs | 42,400 lbs | 75 lbs
70’ | Blue | 17,000 lbs | 21,200 lbs | 42,400 lbs | 81 lbs

## Slide 19: A-22 Cargo Bag

## Slide 20
A22 Cargo Bag
1
1
2
2
3
4
4
5
6
7
Lateral Strap
188” Strap
Scuff Pad
D-Ring
Canvas Cover (Optional)
Medium Suspension Clevis- Rated capacity: 6,250 lbs
24” Suspension Web- Rated capacity: 550 lbs (each)

## Slide 21
2
2
1
1
3
1
1
Lateral Strap
Lacing Cord
188” Strap
Canvas Cover (Optional)
4

## Slide 22
1
2
3
4
Lateral Strap
Lacing Cord
Friction Adapter
Excess Lateral Strap
Canvas Cover (Optional)
5

## Slide 23
1
2
3
Lateral Strap
Friction Adapter
Excess Lateral Strap
Lacing Cord
4

## Slide 24
2
6
1
4
3
5
1
1
1
Lateral Strap
Friction Adapter
188” Strap
Excess 188” Strap
Lacing Cord
Canvas Cover (Optional)
3

## Slide 25
1
3
2
Medium Suspension Clevis
D-Ring
24” Suspension Web- Rated Capacity: 550 lbs