## Slide 1: Fort Carson Snow Removal Plan 2023-2024
Prepared by Doug Homa, Chief, DPW Operations and Maintenance Division
September 2023

## Slide 2: Snow Removal plan – areas
Areas plowed by the DPW operations and maintenance contractor:
  Cantonment area
  Wilderness Road area
  Butts Army Heliport
  Route 1 to Range 143 when needed
Areas plowed by others:
  D8 Schools (D8)
  Housing area internal streets (BBC)
  Motorpools (units)
  Evans Army Community Hospital (Evans Contractor)
  Academy Blvd. & Hwy 115 (CDOT and El Paso County)

## Slide 3: Snow Removal Plan – response plan
  Monitoring: The DPW will monitor weather forecasts in conjunction with Fort Carson Operations Center (FCOC) and send out SITREPS to Garrison leadership in advance of oncoming storms indicating preparations and pretreatment plans.
  Pretreatment: Based on storm predictions, DPW will pre-treat roads with magnesium chloride. Pre-treatment is only applied on hills, curves, intersections and other "hazardous" locations.
  Priority 0 – Special Events
    Throughout all priorities, real world deployment or special event requirements will be addressed immediately.
    Response can take place during normal duty hours and after hours.
  Priority 1 – Main roads, Butts Army Heliport, Public Sidewalks and special areas
    Response can take place during normal duty hours and after hours.
    Special areas will be cleared immediately at first snowfall and throughout storm.
    Government will provide direction to contractor on when to progress to next level of priority based on condition of previous priorities, and conditions of lower priorities areas. However, the lower priority areas may have been cleared from solar melt and traffic prior to having resources available for those lower priorities.

## Slide 4: Snow Removal Plan – response plan (cont)
Priority 2 – Secondary Roads
  Response during normal duty hours only.
Priority 3 – Parking Lots
  Parking lots will not be completely cleared. Only the aisles will be plowed and treated with de-icer.
  Response during normal duty hours only.
  Priorities are in the following general order:
    Fire Stations and Police Stations
    DIV and USAG HQs
    Army Community Service
    Mountain Post Soldier Center (MPSC)
    Medical, Dental and Behavioral Clinics
    DFACs
    Physical Fitness Centers
    Special Events Center
    Elkhorn Conference Center
    Tri-foods

## Slide 5: Snow Removal Plan – response plan (cont)
Limited Response:
  For storms with less than 3” of snow accumulation or ice storms.
  Response will focus on applying de-icer and clearing specific and localized slippery spots by priority order.
  These light storms typically do not create lingering slippery conditions and therefore an extensive or sustained response is not needed.
Full Response:
  For storms with 3” or greater of snow accumulation.
  Response will clear snow from roads in priority order with plows and other heavy equipment.
  Standard measuring points for snowfall: Bldg. 1435 Helipad; Bldg. 8200; Gates 5, 6, 19 and 20; and Bldg. 9601 at Butts Army Heliport.
  Crews will start plowing prior to 3" accumulation if Fort Carson is expected to receive at least 3” by the end of storm.
Delayed Reporting: Allows DPW to get better start on clearing roads before morning rush hour starts. Once cars start arriving and traffic gets heavy, it gets very hard to effectively plow as the snow gets packed and plows get stuck in traffic.

## Slide 6
Snow Removal Plan – Butts Army Heliport
  Intent:
      Keep the main runway (13/31) and taxiway C and ramp C (for crash station access) clear to support 24/7 emergency runway capability.
      Clear taxiways and ramps to meet flying mission priorities and timelines. Use Sidewalks: DPW will clear mainline sidewalks when weather forecasts indicate sustained conditions of snow and ice on the walks.
  Plan:
      DPW will use existing snow removal equipment staged at Bldg. 8200 and will use nylon blades in lieu of steel.
      DPW will pretreat the baseline surfaces (runway13/31 and taxiways Bravo and Charlie) with E36 product, dependent on weather conditions and forecast.
      DPW will clear the baseline surfaces at the onset of snow/ice accumulation 24/7 due to its status as an emergency runway. The trigger for this response will be independent of the snow response for cantonment roads.
      DPW will clear the other taxiways and ramp areas in priority order (as set by Butts Army Heliport base ops based on flying mission requirements) beginning the next normal duty day. Should there be a weekend flying mission, DPW will clear those needed ramps on the weekend as requested by Butts Army Heliport base ops and supported by 4th CAB. All ramps will have to be cleared of aircraft prior to snow removal operations.

## Slide 7: Snow Removal Plan – sidewalks
Common Use Sidewalks: The DPW will clear mainline sidewalks when weather forecasts indicate sustained conditions of snow and ice on the walks.
Building Entrances (50’ Rule): Building occupants are required to clear snow and ice on the sidewalk leading from their doorstep to the first mainline sidewalk, which is typically less than 50’, but could be more.
Facility Managers may draw free Ice Melt from the DPW Supply Warehouse, Bldg. 8100, located off O’Connell Boulevard and Bennett Street on the north end of the cantonment.

## Slide 8
  Sidewalks
  Chapels
    Weekend Services
  Soldier Recovery Unit (SRU) Admin
    Business hours
  SRU Barracks
    24/7
  DFACs
  Child Development Centers
    3” rule
      Parking Lots
      Chapels
        Weekend Services
      SRU Admin and Barracks
        24/7
      Emergency Vehicle Bays
        24/7
      DFAC Loading Docks
      Commissary & Main Exchange
      Shopettes/Expresses
      ASP
      Child Development Centers
        3” rule
Snow Removal Plan – Priority 1 special areas

## Slide 9: snow removal plan – EQUIPMENT
DPW Fleet Equipment
5 Dump trucks w/plow and sander
1 Truck w/mag chloride
1 Truck w/mag chloride and rubber blade for the heliport
7 Graders (1) w/rubber blade for the heliport
3 Tractors w/blades
6 Utility vehicles w/plows (4) w/spreader for sidewalks and parking lots
1 Skidster w/box blade

## Slide 10: SNOW removal plan – RESPONSE COMMO PLAN
T&H Services
1. Alvin Jackson – 719-896-6864
2. Snow Desk – 719-526-5568
COR
Jerald Just – 719-761-2033
Bryan Dorcey – 719-725-8083
DPW
Joe Wyka – 719-244-1152
Doug Homa – 719-491-8596
Scott Clark– 719-726-8852
GC
COL Brown
T&H Services
Shift Supervisor - as listed in SITREP
FCOC
“USARMY Ft Carson IMCOM Central List DPTMS Installation Ops Center”
DES
“USARMY Fort Carson IMCOM Central List DES PPMD Desk“
Desk Sgt. – 719-526-2333
FOD
BBC
DPW
T&H Services Contacts
1. Alvin Jackson – if less than full response
2. Snow Desk – operated during full response
Guidance / Spot Reports
SITREP (generated by DPW)
Direct Coordination when necessary
FCOC = Commo Hub for spot reports
LEGEND
El Paso County
D8

## Slide 11: SNOW removal plan – RESPONSE SITREP
Reports will be generated by T&H Services Shift supervisor.
Reports will be generated before COB on days when storm events are predicted to occur overnight.
Reports will be sent via e-mail body text (and not an attachment) for easy reading on mobile devices.
SITREP 8-LINE FORMAT
Report as of: DTG
Current snow accumulation / ice conditions on roadways:
Driving Conditions:
Active T&H Services response on Cantonment: (monitoring storm, limited ice response, full snow response, snow desk operational, supervisor (name, #), etc.)
Active T&H Services response on Butts Army Heliport: (monitoring storm, limited ice response, full snow response, snow desk operational, supervisor (name, #), etc.)
Significant areas: (list geographic areas of specific concern, heightened efforts, PX/Commissary, railhead, hills, etc.)
Reported by:
Next report due: (every 2 hours during a response)

## Slide 12: Snow removal plan – north map
Emergency Snow Route
Snow Service Roads
Snow Sidewalks

## Slide 13: Snow removal plan – South map
Emergency Snow Route

## Slide 14
snow removal plan – Butts Army Heliport

## Slide 15: Snow removal plan – contacts
T&H Services 24/7 Service Order Desk – 719-526-5345
Fort Carson Operations Center (FCOC) – 719-526-3400/5500
Butts Army Heliport Weather Station – 719-526-3620
Fort Carson Dispatch – 719-526-2333